## Slide 1
Introduction:
Bicycle theft is a major problem in many cities, especially university towns.
Our aim was to create a system that enables a bike owner to track a stolen bike. While other systems already on the market are trying to accomplish this by using GSM modules we tried to use a minimalistic approach:
A tracking GPS module that can be turned on when a bike has been stolen, tracks positions and retransmits them to the user via a short distance wireless interface.
Used Hardware:
PC
Iris Mote (Nummer)
GPS Module (Nummer)
Used Software:
Tiny OS
Linux (Distro)
Node JS with Express
MongoDB
Drip Protocol (Source?)
▪ Collection of Position Logs
▪ Dissemination of Array with ID‘s of stolen bikes
System Description
The system consits of a PC running a webserver, a iris mote connected to the PC via USB, a set of relay IRIS motes and so called bike iris motes. The process begins with a user marking his bike as stolen using the system‘s webapp using an ID. The webserver will relay this ID to the basestation which broadcasts it to all relay motes via dissemination. When a bike passes a relay mote it will establish a connection and check whether its ID was disseminated. If this was the case the bike mote will turn on its GPS module and start recording its position in combination with a timestamp.
The next time the bike passes a relay mote the position data will be transfered, collected at the base station and made available to the user on the webapp
Conclusion:
The system we proposed an implemented prototypically allows a user to remotely turn on a location tracking device, collect data over extended periods of time. This works even if his bike is not in range of a network after it has been activated. Using a easy to use webinterface bikes and be quickly reported as stolen and location data can be conveniently displayed on a digital map.
Future work is needed to determine how battery usage can be minimized (e.g. by replacing GPS with WiFi positioning) and whether a sufficient relay network can be established at reasonable costs.